## Slide 1
ASTOS Model Setup –
Sub-Orbital Rocket Trajectory Modelling
Jason Ong

## Slide 2
High Level Overview
Modular
Component Integration
Model Integration
Planet model (Earth)
Atmospheric model (US 76)
Wind model (custom or generic)
Thrust curve
Aerodynamic tables
Aerothermal data (not required for now)
Masses and dimensional data
Sensors (IMU etc.) (not required for now)
Trajectory Phase Settings

## Slide 3
Performance definition variations
Typically vacuum thrust and mass flow is selected
For simplification, mass flow is usually set as constant value
Thrust Model

## Slide 4
General Thrust Equation
For vacuum thrust,
,
For sea level thrust,
= 100 kPa
Conversion of SL thrust to vacuum thrust:
Propulsion thrust curve data
Vacuum thrust curve data as Astos input
Nozzle exhaust area as input
Thrust Model

## Slide 5
Nozzle exhaust area = 0
Nozzle exhaust area ≠ 0
Total Thrust = Vacuum Thrust
Thrust Model

## Slide 6
Thrust Model
Chart: Time (s)
SL Thrust | 0 | 10.14 | 26.295 | 25.172 | 24.403 | 23.847 | 22.974 | 22.696 | 22.476 | 22.293 | 21.999 | 21.482 | 21.3 | 21.117 | 20.819 | 20.555 | 20.304 | 20.063 | 19.824 | 19.581 | 19.333 | 19.079 | 18.811 | 18.536 | 18.256 | 0
Thrust (2-DoF) | 0 | 26.252 | 25.131 | 24.364 | 23.811 | 22.942 | 22.001 | 21.539 | 21.249 | 21.045 | 20.891 | 20.764 | 20.659 | 20.564 | 20.472 | 20.38 | 20.284 | 20.175 | 20.057 | 19.932 | 0

## Slide 7
Aerodynamics Model
Force and moment equations in body-fixed coordinates

## Slide 8
Aerodynamics Model
Moment Coefficients Computation (Astos Model Reference)
Currently Used

## Slide 9
Aerodynamics Model
For rotational symmetry, we assume:
=
=
Equivalent notations when compared to other literature:
− CNA
− Cyβ
− CLP
− CLδ
− CMQ
− CNR

## Slide 10
Aerodynamics Model
Definition of Reference Quantities
XCP point is relative to where global node is positioned.
Length and area

## Slide 11
Aerodynamics Model
In this case, XCP is defined +ve since global node is at the bottom. In the case where global node is placed at tip of nose, XCP should be defined –ve.
Global Node Placement

## Slide 12
Aerodynamics Model
1D Interpolation
1st column : Mach (Values must be monotonically increasing)
2nd column: Xcp

## Slide 13
Aerodynamics Model
2D Interpolation
1
2
Data

## Slide 14
Aerodynamics Model
2D Interpolation (according to Astos)

## Slide 15
Aerodynamics Model
CNA
Cyβ
CLP
CLδ
CMQ
CNR
CD
Coefficients

## Slide 16
Aerodynamics Model
Fin Cant
Define fin cant angle

## Slide 17
Vehicle Definition
Specify components in use
Define component position using anchor node placement, and position/rotation offsets

## Slide 18
Vehicle Definition
For specifying thrust misalignments during Monte Carlo simulations

## Slide 19
Phase Definition
Overall
Timestep
Phase selection for trajectory simulation

## Slide 20
Phase Definition
Ignition Phase
Ignition start time on thrust curve

## Slide 21
Phase Definition
No. of phases vary from case to case, depends on dynamics of trajectory phases
Boolean condition: phase ends when altitude > launch rail height
“Enabled” for boolean condition to work
Phase ends when
Boolean condition is reached, OR
Phase span reaches mission time or phase time defined
Rail Phase

## Slide 22
Phase Definition
Thrust Phase
End time on thrust curve

## Slide 23
Phase Definition
Boolean condition: phase ends when altitude > 30 km
Coast Phase

## Slide 24
Phase Definition
Boolean condition: phase ends when altitude < 0 km
2nd Coast Phase

## Slide 25
Trajectory Parameters
Initial State
Lat, long, alt
Speed, inclination, heading

## Slide 26
Trajectory Parameters
Default Settings
Default aerodynamics model: No base drag

## Slide 27
Trajectory Parameters
Default Settings
Default equation of motion and attitude control laws used

## Slide 28
Trajectory Parameters
Equations of Motion: Inertial Velocity(Astos Model Reference)

## Slide 29
Trajectory Parameters
Default Settings
Default CoM

## Slide 30
Trajectory Parameters
Default Settings
Default MoI (YY) (Same for ZZ)

## Slide 31
Trajectory Parameters
Default Settings
Default MoI (XX)

## Slide 32
Trajectory Parameters
Default Settings
CoM
MoI - XX
MoI - YY
Verification of default settings

## Slide 33
Trajectory Parameters
Dynamics - Ignition
Active motor

## Slide 34
Trajectory Parameters
Dynamics - Ignition

## Slide 35
Trajectory Parameters
Equations of Motion: Launch Pad (Astos Model Reference)

## Slide 36
Trajectory Parameters
Dynamics - Rail
Active motor

## Slide 37
Trajectory Parameters
Dynamics - Rail

## Slide 38
Trajectory Parameters
Equations of Motion: Accelerate Flight Path (Astos Model Reference)

## Slide 39
Trajectory Parameters
Dynamics - Rail
Active motor

## Slide 40
Trajectory Parameters
Dynamics - Thrust
Active motor

## Slide 41
Trajectory Parameters
Dynamics - Coast
Inactive motor
Full base drag – 0 km altitude

## Slide 42
Trajectory Parameters
Dynamics – 2nd Coast Phase
Inactive motor
Full base drag – 30 km altitude

## Slide 43
Modelling Guidelines
Focus on a single phase at a time
  Disable later phases in the “Phases & Common Settings”
Use curve plots in the “Results” panel for verifying correctness of input/output data
Large aerodynamic tables (i.e. 2D) can be split into series of 1D tables for simulation
  Consequently, the same increase in the no. of trajectory phases are required since each phase utilizes a different aerodynamic table